## Slide 1: JNCIS-ENT
Layer 2 switching and VLANs

## Slide 2: L2 Troubleshooting and Maintenance
L2 configuration and maintenance commands
7

## Slide 3: EX Management Interfaces
EX Series switches provide an OOB management interface me0 along with the console serial port.
  Configure an IP on the me0 interface for remote OOB management
me0 interface
Serial interface
{master:0}[edit interfaces]
user@Switch# show me0
unit 0 {
family inet {
address 10.0.0.10/24;
}
}

## Slide 4: Enable L2 Switching
Use the family ethernet-switching command on an interface or interface range to enable basic L2 switching functionality.
{master:0}[edit interfaces]
user@Switch# show
ge-0/0/0 {
unit 0 {
family ethernet-switching;
}
}
ge-0/0/1 {
unit 0 {
family ethernet-switching;
}
}
…
{master:0}[edit interfaces]
user@Switch# show
interface-range switchports-1 {
member ge-0/0/0;
member ge-0/0/1;
member ge-0/0/2;
unit 0 {
family ethernet-switching;
}
}
…

## Slide 5: EX Interface Status
Use the show interfaces terse command to verify interface status and mode
{master:0}
user@Switch> show interfaces terse | match “interface|0/0|0/1”
Interface Admin Link Proto Local Remote
ge-0/0/0 up up
ge-0/0/0.0 up up eth-switch
ge-0/0/1 up up
ge-0/0/1.0 up up eth-switch

## Slide 6: Bridge Table Status
Use the show ethernet-switching table command to view the contents of the bridge table
{master:0}
user@Switch> show ethernet-switching table
…
Ethernet switching table : 3 entries, 3 learned
Routing instance : default-switch
Vlan MAC MAC Age Logical
name address flags interface
    default 00:11:22:aa:aa:aa D - ge-0/0/1.0
    default 00:11:22:bb:bb:bb D - ge-0/0/2.0
    default 00:11:22:cc:cc:cc D - ge-0/0/3.0
Switch

## Slide 7: MAC Forwarding Table Status
Use the show route forwarding-table family ethernet-switching command to view the contents of the forwarding table
{master:0}
user@Switch> show route forwarding-table family ethernet-switching
Routing table: default-switch.bridge
VPLS:
Destination Type RtRef Next hop Type Index NhRef Netif
default perm 0 dscd 1300 1
ge-0/0/0.0 intf 0 ucst 1332 4 ge-0/0/0.0
ge-0/0/1.0 intf 0 ucst 1333 6 ge-0/0/1.0
Routing table: default-switch.bridge
Bridging domain: v950.bridge
VPLS:
Enabled protocols: Bridging, ACKed by all peers,
Destination Type RtRef Next hop Type Index NhRef Netif
00:03:00:00:00:a0/48 user 0 ucst 1333 6 ge-0/0/1.0
00:03:00:00:fc:96/48 user 0 ucst 1332 4 ge-0/0/0.0

## Slide 8: Clear Bridging Table
Use the clear ethernet-switching table command to clear entries from the bridge table
{master:0}
user@Switch> show ethernet-switching table
…
Ethernet switching table : 2 entries, 2 learned
Routing instance : default-switch
Vlan MAC MAC Age Logical NH RTR
name address flags interface Index ID
v950 00:a0:9c:01:bf:1c D - ge-0/0/1.0 0 0
v950 fc:96:43:88:f2:26 D - ge-0/0/0.0 0 0
{master:0}
user@Switch> clear ethernet-switching table interface ge-0/0/1
{master:0}
user@Switch> show ethernet-switching table
…
Ethernet switching table : 1 entries, 1 learned
Routing instance : default-switch
Vlan MAC MAC Age Logical NH RTR
name address flags interface Index ID
v950 fc:96:43:88:f2:26 D - ge-0/0/0.0 0 0

## Slide 9: Defining Static Table Entries
Static bridge table entries can be defined under the [edit vlans] hierarchy of the configuration.
{master:0}[edit vlans]
user@Switch# show
v950 {
vlan-id 950;
switch-options {
interface ge-0/0/2.0 {
static-mac 00:11:22:33:44:55;
}
}
}
{master:0}
user@Switch> show ethernet-switching table
…
Ethernet switching table : 2 entries, 2 learned
Routing instance : default-switch
Vlan MAC MAC Age Logical NH RTR
name address flags interface Index ID
v950 00:a0:9c:01:bf:1c D - ge-0/0/1.0 0 0
v950 fc:96:43:88:f2:26 D - ge-0/0/0.0 0 0
v950 00:11:22:33:44:55 S - ge-0/0/2.0 0 0