## Slide 1: JNCIS-ENT
Layer 2 switching and VLANs

## Slide 2: Configuring and Verifying VLANs
Junos VLAN commands
10

## Slide 3: The Default VLAN
Default EX configuration enables all switchports and associates them with the default VLAN
  An asterisk (*) indicates the interface is active
  The default VLAN ID maybe be changed using the set vlans default vlan-id command
{master:0}
user@switch> show vlans
Routing instance VLAN name Tag Interfaces
default-switch default 1
ge-0/0/0.0*
ge-0/0/1.0*
{master:0}
user@switch# set vlans default vlan-id 100
{master:0}
user@switch> show vlans
Routing instance VLAN name Tag Interfaces
default-switch default 100
ge-0/0/0.0*
ge-0/0/1.0*

## Slide 4: Configuring VLANs
VLANs are configured in the edit vlans configuration hierarchy
{master:0} [edit vlans]
user@switch# show
default {
vlan-id 1;
}
v950 {
description "MGMT";
vlan-id 950;
}

## Slide 5: Configuring Access Ports
Access ports are configured by setting the interface-mode access command at the edit interfaces <intf> unit 0 family ethernet-switching hierarchy
{master:0} [edit]
user@switch# show interfaces ge-0/0/0
description USER;
unit 0 {
family ethernet-switching {
interface-mode access;
vlan {
members default;
}
}
}
{master:0} [edit]
user@switch# show interfaces ge-0/0/1
description MGMT;
unit 0 {
family ethernet-switching {
interface-mode access;
vlan {
members v950;
}
}
}

## Slide 6: Verifying VLAN Assignments
Use the show vlans operational mode command to verify VLAN configuration
  An asterisk (*) indicates the interface is active
{master:0}
user@switch> show vlans
Routing instance VLAN name Tag Interfaces
default-switch default 1
ge-0/0/0.0*
default-switch v950 950
ge-0/0/1.0*