## Slide 1: JNCIS-ENT
Layer 2 switching and VLANs

## Slide 2: Inter-VLAN Routing
Integrated routing and bridging interfaces (IRBs)
12

## Slide 3: What is an IRB?
An integrated routing and bridging (IRB) interface is a layer 3 logical interface that facilitates inter-VLAN routing.
Switch
frame
VLAN 10
VLAN 10
VLAN 20
irb.10
irb.20

## Slide 4: Where are IRBs
Due to IRBs supporting routing for a broadcast domain, they are usually implemented at the access layer or aggregation/distribution layer
Core
Aggregation
Access

## Slide 5: Configuring IRBs
A separate IRB interface must be configured for each VLAN the switch will route for
  Once configured, the IRB interfaces function as a standard L3 interface and may be placed in separate routing instances or have filtering applied via firewall policies.
{master:0} [edit]
user@switch# show interfaces irb
unit 10 {
family inet {
address 10.1.10.1/24;
}
}
unit 20 {
family inet {
address 10.1.20.1/24;
}
}
Switch
VLAN 10 User
10.1.10.105/24
VLAN 10 User
10.1.10.110/24
VLAN 20 User
10.1.20.54/24
irb.10
irb.20

## Slide 6: Associating IRBs with VLANs
A VLAN must be associated to an IRB interface to allow the IRB to route for the specified broadcast domain
  The VLAN must have at least 1 operational member interface before the associated IRB will become operational
{master:0} [edit]
user@switch# show vlans
Default{
vlan-id 1;
}
Vlan10{
vlan-id 10;
l3-interface irb.10;
}
Vlan20 {
vlan-id 20;
l3-interface irb.20;
}
Switch
VLAN 10 User
10.1.10.105/24
VLAN 10 User
10.1.10.110/24
VLAN 20 User
10.1.20.54/24
irb.10
irb.20

## Slide 7: Validating IRBs
user@switch> show interfaces terse irb
Interface Admin Link Proto Local Remote
irb up up
irb.10 up down inet 10.1.10.1/24
irb.20 up down inet 10.1.20.1/24
user@switch> show vlans
Routing instance VLAN name Tag Interfaces
default-switch default 1
default-switch vlan10 10
default-switch vlan20 20
user@switch> show interfaces terse irb
Interface Admin Link Proto Local Remote
irb up up
irb.10 up up inet 10.1.10.1/24
irb.20 up up inet 10.1.20.1/24
user@switch> show vlans
Routing instance VLAN name Tag Interfaces
default-switch default 1
default-switch vlan10 10
ge-0/0/1.0*
default-switch vlan20 20
ge-0/0/2.0*

## Slide 8: Validating Routing
user@switch> show route 10.1/16
inet.0: 7 destinations, 7 routes (7 active, 0 holddown, 0 hidden)
+ = Active Route, - = Last Active, * = Both
10.1.10.0/24 *[Direct/0] 00:03:44
> via irb.10
10.1.10.1/32 *[Local/0] 00:03:44
Local via irb.10
10.1.20.0/24 *[Direct/0] 00:03:44
> via irb.20
10.1.20.1/32 *[Local/0] 00:03:44
Local via irb.20