## Slide 1: JNCIS-ENT
Layer 2 security and loop prevention

## Slide 2: Loop Prevention
How loops are formed and affect a network
1

## Slide 3: What is a loop?
A forwarding loop occurs when a single broadcast domain is connected in such a way that a physical/logical loop is formed, and a frame is flooded
  A frame’s header does not contain any attributes to prevent it from being forwarded forever, as such if a loop is formed, a broadcast frame will be forwarded in the loop until the loop is broken.
Flood
broadcast
Flood
Flood
Layer 2
Loop
Preamble
Destination Address
Source Address
Type
Data
FCS

## Slide 4: Preventing loops
Loops can be prevented manually by simply avoiding connecting switches in a loop however, this is unreliable due to human error.
Protocols in a Spanning Tree Protocol family are designed to create the most efficient loop-free topology in a layer 2 forwarding domain.
  STP is defined in IEEE 802.1D-1998
  RSTP is defined in IEEE 802.1w-2004
  MSTP and VSTP are not covered as part of the JNCIS-ENT
Flood
broadcast
Flood
Flood
Loop Free
X

## Slide 5: STP Overview
STP follows a high-level 4-step process to create a loop-free topology (a spanning tree)
  Switches exchange bridge protocol data units (BPDUs)
  A root bridge is elected
  Port roles and states and determined
  Tree is fully converged
Flood
broadcast
Flood
Flood
Loop Free
X

## Slide 6: STP Terms
Bridge ID (BID)
  A BID is composed of a priority value and the switch’s system MAC address
  The lowest BID is used to elect a root bridge
Bridge Protocol Data Unit (BPDU)
  BPDUs are exchanged between switches and contain the Port ID, Port Priority and BID, among other fields
Designated / Root Ports
  Designated ports are ports which will be in a forwarding state and are not a root port
  Root ports are ports which are connected to the shortest path to the root bridge
Root Bridge
  A switch which advertises the lowest BID and has been elected as the root of the spanning tree
Designated Bridge
  A switch within the LAN which is not the root bridge