## Slide 1: JNCIS-ENT
Layer 2 security and loop prevention

## Slide 2: Rapid Spanning Tree Protocol
Improvements in 802.1w
3

## Slide 3: Differences From STP
RSTP provides faster (re)convergence time
  Links can be designated as Point-to-Point (P2P) links which can transition from Blocking to Forwarding without waiting
  Ports can be designated as Edge ports which are always in a forwarding state
  Reconvergence can allow for a new root port to transition to forwarding state without waiting for protocol timers to expire
RSTP can detect indirect link failure and recover without waiting for the Root Bridge notification
2 new port roles are introduced
  Alternate port
    Essentially a backup root port
  Backup port
    Essentially a backup designated port

## Slide 4: RSTP Port Roles
Alternate Port
  Is an alternate, higher cost, path to the root
  If in a shared LAN segment, the non-designated bridge will have alternate ports
  Alternate Ports block traffic while receiving superior BPDUs from a neighboring switch
Backup Port
  Only present on designated switches
  Provide a backup path to a shared LAN segment
  The lowest port ID will be a designated port, the remaining will be backup ports
SW2
Designated Bridge
SW1 Root Bridge
SW3
D
D
D
D
R
R
A
A
A
A
D
B

## Slide 5: Port States
RSTP combines the Blocking and Listening port states in STP into Discarding
STP 802.1D | RSTP 802.1w
Blocking | Discarding
Listening | 
Learning | Learning
Forwarding | Forwarding

## Slide 6: RSTP BPDUs
All RSTP switches send configuration BPDUs every 2 seconds
RSTP uses BPDUs as a keepalives
  Allows for detection of failures in 6 seconds (3x hello interval)
Switchports operating in full-duplex are considered P2P ports
  Can transition from a non-root or non-designated to a root or designated without waiting for the timers to expire
Switchports operating in half-duplex are considered shared links
SW2
Designated Bridge
SW1 Root Bridge
SW3
D
D
D
D
R
R
A
A
A
A
D
B

## Slide 7: BPDU Format
Protocol ID [2]
Protocol Version [1]
BPDU Type [1]
Flags [1]
Root ID [8]
Root Path Cost [4]
Bridge ID [8] =
Priority [2] +
Bridge Address [6]
Port ID [1]
Port number [1] +
Port ID [2] =
Message Age [2]
Max Age [2]
Hello Time [2]
Forward Delay [2]
Version 1 Length [2]
RSTP is backwards compatible with STP
RSTP devices detect the type of BPDU using the Protocol Version and BPDU Type fields
4 Fields differ in RSTP from STP:
  Protocol Version
  BPDU Type
  Flags
  Version 1 Length (not present in STP BPDU)

## Slide 8: BPDU Flags
Protocol ID [2]
Protocol Version [1]
BPDU Type [1]
Flags [1]
Root ID [8]
Root Path Cost [4]
Bridge ID [8] =
Priority [2] +
Bridge Address [6]
Port ID [1]
Port number [1] +
Port ID [2] =
Message Age [2]
Max Age [2]
Hello Time [2]
Forward Delay [2]
Version 1 Length [2]
Bit 1: Topology Change
  Used to notify other switches the topology has changed
Bit 2: Proposal
  Used to help transition a designated port to forwarding
Bits 3 and 4: Port Role
  Specifies the role of the sending port
  0 = unknown, 1= alternate or backup, 2=root, 3=designated
Bit 5: Learning
  Used to advertise that the port is in learning state
Bit 6: Forwarding
  Used to advertise that the port is in forwarding state
Bit 7: Agreement
  Used in response to proposal flag to transition a designated port
Bit 8: TCN Acknowledgement
  Used in STP to acknowledge TCNs

## Slide 9: RSTP Convergence (1)
Configuration BPDUs are flooded by each switch
  All ports are initially Designated Discarding ports
  SW1 will send its superior BPDUs from its Designated Discarding port with Proposal bit set to SW2
  After receiving a superior BPDU, SW2 concludes that this port is the Root port. SW2 will transition this port from Designated Discarding to Root Discarding.
  as a result of receiving a Proposal on a Root port, SW2 will put all non-edge Designated ports into the Discarding state. This is the Sync operation.
SW1 Root Bridge
SW2
SW1 Root Bridge
SW2
R,D
D,D
SW3
SW3
D,D
D,D
D,D
Proposal

## Slide 10: RSTP Convergence (2)
After all non-edge Designated ports are put into Discarding state, SW2 send an Agreement back to SW1 and moves the Root Discarding port into Root Forwarding
Upon receiving the Agreement from SW2, SW1 will move its Designated Discarding port to Designated Forwarding
On SW2, ports that have been put into Designated Discarding state as the result of the Sync operation, will start sending their own Proposals, propagating the convergence further down the network
This proposal and agreement process continues until all switches have converged
SW1 Root Bridge
SW2
R,F
D,F
SW3
D,D
Agreement
D,D
Proposal

## Slide 11: Indirect Link Failure
From SW3’s perspective, when the indirect link failure occurs:
  SW2’s root port fails and SW2 assumes it is now the root
  SW3 receives inferior BPDUs from SW2 and transitions Alternate Port to Designated, sends a proposal superior BPDU
  SW2 responds with an agreement and transitions port to Root Port role
SW2
SW1 Root Bridge
SW3
D
D
R
R
A
D
SW2
SW1 Root Bridge
SW3
D
D
R
R
X
Inferior BPDU
proposal agreement