## Slide 1: JNCIS-ENT
Layer 2 security and loop prevention

## Slide 2: Configuring STP and RSTP
Configuration and monitoring commands
4

## Slide 3: Default STP Settings
STP is configured in the rstp configuration hierarchy
Configuration shown illustrates default STP values
{master:0} [edit protocols rstp]
user@switch# show
bridge priority 32k;
max-age 20;
hello-time 2;
forward-delay 15;
interface ge-0/0/1;
interface ge-0/0/2;
force-version stp;

## Slide 4: RSTP Configuration
STP is configured in the rstp configuration hierarchy
Configuration shown illustrates default STP values
  Max-age and forward-delay are dynamically set to what is advertised by elected Root
{master:0} [edit protocols rstp]
user@switch# show
bridge priority 32k;
max-age 20;
hello-time 2;
forward-delay 15;
interface ge-0/1/0 {
cost 20000;
mode point-to-point;
}
interface ge-0/0/2 {
edge;
}
Switch Root Bridge
Switch2
R,F
D,F
Notes: NOTE: in Enhanced Layer 2 Software (ELS) you can no longer specify “interface all”, each interface must be explicitly defined.

## Slide 5: Monitoring STP
user@switch> show spanning-tree bridge
STP bridge parameters
Routing instance name : GLOBAL
Context ID : 0
Enabled protocol : STP
Root ID : 32768.4c:96:14:71:0b:50
Hello time : 2 seconds
Maximum age : 20 seconds
Forward delay : 15 seconds
Message age : 0
Number of topology changes : 0
Local parameters
Bridge ID : 32768.4c:96:14:71:0b:50
Extended system ID : 0
{master:0} [edit protocols rstp]
user@switch# show
interface ge-0/0/1;
force-version stp;
Notes: increasing topology changes indicates a loop or flapping link

## Slide 6: Monitoring STP
{master:0} [edit protocols rstp]
user@switch# show
interface ge-0/0/1;
force-version stp;
user@switch> show spanning-tree interface
Spanning tree interface parameters for instance 0
Interface Port ID Designated Designated Port State Role
port ID bridge ID Cost
ge-0/0/1 128:2 128:2 32768.4c9614710b50 20000 FWD DESG

## Slide 7: Monitoring RSTP
user@switch> show spanning-tree bridge
STP bridge parameters
Routing instance name : GLOBAL
Context ID : 0
Enabled protocol : RSTP
Root ID : 32768.4c:96:14:71:0b:50
Hello time : 2 seconds
Maximum age : 20 seconds
Forward delay : 15 seconds
Message age : 0
Number of topology changes : 0
Local parameters
Bridge ID : 32768.4c:96:14:71:0b:50
Extended system ID : 0
{master:0} [edit protocols rstp]
user@switch# show
interface ge-0/0/1;
interface ge-0/0/2 {
edge;
}
Switch Root Bridge
Switch2
R,F
D,F
Notes: increasing topology changes indicates a loop or flapping link

## Slide 8: Monitoring RSTP
{master:0} [edit protocols rstp]
user@switch# show
interface ge-0/0/1;
user@switch> show spanning-tree interface
Spanning tree interface parameters for instance 0
Interface Port ID Designated Designated Port State Role
port ID bridge ID Cost
ge-0/0/1 128:2 128:2 32768.4c9614710b50 20000 FWD DESG
user@switch2> show spanning-tree interface
Spanning tree interface parameters for instance 0
Interface Port ID Designated Designated Port State Role
port ID bridge ID Cost
ge-0/0/2 128:3 128:3 32768.4c9614710b51 20000 FWD ROOT
{master:0} [edit protocols rstp]
user@switch2# show
interface ge-0/0/2;