## Slide 1: JNCIS-ENT
Protocol Independent Routing

## Slide 2: Routing instances and RIB groups
Administratively configured routing
3

## Slide 3: What is a Routing Instance?
A routing instance is a collection of independent route tables, interfaces and protocols
  The default routing instance is where all interfaces, tables and protocols operate by default.
  Routing instances are administratively configured, typically to separate routing operations
Interfaces are individually configured within a non-default routing instance
  Configured instances may have entirely different routing tables
Default instance | Customer 1 instance | Customer 2 instance
inet.0 | cust1.inet.0 | cust2.inet.0
ge-0/0/0.100 | ge-0/0/0.200 | ge-0/0/0.300
Default route 1 | Default route 2 | Default route 3
OSPF instance 1 | OSPF instance 2 | OSPF instance 3

## Slide 4: The Default Routing Instance
lab@SW1> show route instance
Instance Type
Primary RIB Active/holddown/hidden
master forwarding
inet.0 3/0/1
inet6.0 1/0/0
__juniper_private1__ forwarding
__juniper_private1__.inet.0 6/0/0
__juniper_private2__ forwarding
__juniper_private2__.inet.0 0/0/1
__master.anon__ forwarding
mgmt_junos forwarding
The default routing instance is also known as the master routing instance
Notes: Inet6.0 table indicates presence of IPv6 routes/forwarding

## Slide 5: Routing Instance Types
Routing instances are typically used for system virtualization or VPN services
  Available instance types vary by platform, aways check documentation
lab@SW1# set routing-instances example_instance instance-type ?
Possible completions:
evpn EVPN routing instance
evpn-vpws EVPN VPWS routing instance
forwarding Forwarding instance
l2backhaul-vpn L2Backhaul/L2Wholesale routing instance
l2vpn Layer 2 VPN routing instance
layer2-control Layer 2 control protocols
mpls-forwarding Routing instance provides a MPLS forwarding-context
mpls-internet-multicast Internet Multicast over MPLS routing instance
no-forwarding Nonforwarding instance
virtual-router Virtual routing instance
vpls VPLS routing instance
vrf Virtual routing forwarding instance

## Slide 6: Configuring Routing Instances
lab@SW1> show configuration routing-instances
customer_A {
routing-options {
static {
route 0.0.0.0/0 next-hop 10.22.33.1;
}
}
protocols {
ospf {
area 0.0.0.0 {
interface ge-0/0/2.0;
}
}
}
interface ge-0/0/2.0;
instance-type virtual-router;
}
Interfaces must be explicitly added to a routing-instance
Separate dynamic routing protocol instances exist in routing-instances

## Slide 7: Working with Routing Instances
lab@SW1> ping 10.22.33.2 routing-instance customer_A rapid count 10
PING 10.22.33.2 (10.22.33.2): 56 data bytes
!!!!!!!!!!
--- 10.22.33.2 ping statistics ---
10 packets transmitted, 10 packets received, 0% packet loss
round-trip min/avg/max/stddev = 0.010/0.014/0.043/0.010 ms
lab@SW1> show interfaces terse routing-instance customer_A
Interface Admin Link Proto Local Remote
ge-0/0/2.0 up up inet 10.22.33.2/26
lab@SW1> show route table customer_A.inet.0
customer_A.inet.0: 4 destinations, 4 routes (4 active, 0 holddown, 0 hidden)
+ = Active Route, - = Last Active, * = Both
0.0.0.0/0 *[Static/5] 00:01:05
> to 10.22.33.1 via ge-0/0/2.0
…

## Slide 8: What is a RIB Group?
RIB groups are used for sharing routes between routing instances
  Commonly used for Filter-based forwarding and VPNs
Routes are imported from a protocol to one or more tables
  A policy may be applied to narrow which routes are imported
Routes are exported from a table to a protocol
  The export-rib statement is used to sharing routes with a protocol neighbor from a non-native table
Instance Table 1
Instance Table 2
Routes

## Slide 9: Configuring RIB Groups
lab@SW1> show configuration routing-instances
customer_A {
routing-options {
static {
route 0.0.0.0/0 next-hop 10.22.33.1;
}
interface-routes {
rib-group inet group1;
}
}
protocols {
ospf {
area 0.0.0.0 {
interface ge-0/0/2.0;
}
}
}
interface ge-0/0/2.0;
instance-type virtual-router;
}
lab@SW1> show configuration interfaces ge-0/0/2
unit 0 {
family inet {
address 10.22.33.2/26;
}
}
lab@SW1> show configuration routing-options rib-groups
group1 {
import-rib [ customer_A.inet.0 inet.0 ];
}
Notes: Note that ge-0/0/2.0 is in the customer_A routing-instance and the IP is 10.22.33.2/26. Note that the rib0group needs to be applied in the source instance

## Slide 10: Configuring RIB Groups
lab@SW1> show route
inet.0: 6 destinations, 6 routes (5 active, 0 holddown, 1 hidden)
+ = Active Route, - = Last Active, * = Both
10.22.33.0/26 *[Direct/0] 00:00:03
> via ge-0/0/2.0
10.22.33.1/32 *[Direct/0] 1d 01:27:08
> via lo0.0
10.22.33.2/32 *[Local/0] 00:00:03
Local via ge-0/0/2.0
192.168.2.0/24 *[Direct/0] 3d 19:37:59
> via ge-0/0/0.0
192.168.2.212/32 *[Local/0] 3d 19:37:59
Local via ge-0/0/0.0
customer_A.inet.0: 4 destinations, 4 routes (4 active, 0 holddown, 0 hidden)
+ = Active Route, - = Last Active, * = Both
0.0.0.0/0 *[Static/5] 00:00:03
> to 10.22.33.1 via ge-0/0/2.0
10.22.33.0/26 *[Direct/0] 00:50:49
> via ge-0/0/2.0
10.22.33.2/32 *[Local/0] 00:50:49
Local via ge-0/0/2.0
224.0.0.5/32 *[OSPF/10] 00:56:58, metric 1
MultiRecv