## Slide 1: JNCIS-ENT
Protocol Independent Routing

## Slide 2: Filter Based Forwarding
Routing with more than the destination address
5

## Slide 3: What is Filter Based Forwarding?
Filter based forwarding uses firewall filters to match traffic and make forwarding decisions
  This allows for more fields than the destination address to be used to make forwarding decisions, such as the source address
Filter based forwarding is accomplished by redirecting traffic to another routing-instance which contains the desired destination-based routing information
  RPF checks aren’t supported with FBF
  3 steps to configure FBF:
Match traffic
Use a firewall filter at the ingress interface to match traffic that should be forwarded in a different manner
Define routing
Create routing instances for each set of matched traffic of type ‘forwarding’.
Share interfaces
Create and apply a RIB group to share the default routing instance interface routes with the custom instances.

## Slide 4: Step 1: Match Traffic
Create and apply an inet firewall filter to match the traffic.
  Example will be to route based on source IP address
lab@SW1# show firewall
family inet {
filter my_fbf_filter {
term test_term1 {
from {
source-prefix-list {
fbf_prefix_1;
}
}
then {
routing-instance ISP_A;
}
}
term test_term2 {
then {
accept;
}
}
}
}
lab@SW1# show policy-options
prefix-list fbf_prefix_1 {
192.168.3.0/24;
}
lab@SW1# show interfaces ge-0/0/0.0
family inet {
filter {
input my_fbf_filter;
}
address 192.168.2.212/24;
}

## Slide 5: Step 2: Define Routing
Create a forwarding type routing-instance with the desired routing information
  In this case the custom routing-instance has a different default route than the default instance
lab@SW1# show routing-instances
ISP_A {
routing-options {
static {
route 0.0.0.0/0 next-hop 192.168.2.2;
}
}
instance-type forwarding;
}
lab@SW1# show routing-options
interface-routes {
rib-group inet fbf_ribgroup;
}
rib-groups {
fbf_ribgroup {
import-rib [ inet.0 ISP_A.inet.0 ];
}
}

## Slide 6: Step 3: Share Interfaces
Create a RIB group to allow the custom routing information next-hops to be resolvable.
  Recall that the rib-group is applied in the instance from which the routing information should be shared.
lab@SW1# show routing-options
interface-routes {
rib-group inet fbf_ribgroup;
}
rib-groups {
fbf_ribgroup {
import-rib [ inet.0 ISP_A.inet.0 ];
}
}
lab@SW1> show route
inet.0: 5 destinations, 5 routes (5 active, 0 holddown, 0 hidden)
+ = Active Route, - = Last Active, * = Both
0.0.0.0/0 *[Static/5] 00:17:00
> to 192.168.2.1 via ge-0/0/0.0
192.168.2.0/24 *[Direct/0] 4d 21:52:34
> via ge-0/0/0.0
192.168.2.212/32 *[Local/0] 4d 21:52:34
Local via ge-0/0/0.0
ISP_A.inet.0: 6 destinations, 6 routes (6 active, 0 holddown, 0 hidden)
+ = Active Route, - = Last Active, * = Both
0.0.0.0/0 *[Static/5] 00:17:00
> to 192.168.2.2 via ge-0/0/0.0
192.168.2.0/24 *[Direct/0] 00:17:00
> via ge-0/0/0.0
192.168.2.212/32 *[Local/0] 00:17:00
Local via ge-0/0/0.0