## Slide 1: JNCIS-ENT
Intermediate System to Intermediate System (IS-IS)

## Slide 2: Configuring IS-IS
Configuring interfaces and protocols for IS-IS
5

## Slide 3: Configuration Requirements
Loopback ISO family and NET address configured
  At least 1 NET address is needed for setting the System ID for IS-IS, Juniper recommends using the loopback interface
ISO protocol family on logical interfaces running IS-IS
  No NET/NSAP address needed on individual interfaces
IS-IS protocol configuration with interfaces to run IS-IS
  Individual interfaces may be configured to send L1 or L2 or both L1/L2 PDUs
  L1/L2 is the default configuration
On SRXs ISO family forwarding mode must be set to packet-based
  Even if the MPLS family forwarding mode is set to packet-based, the ISO family forwarding mode is set separately

## Slide 4: 1. Loopback ISO NET Address
Any interface may be used to supply a NET address for the System ID for IS-IS though using the Loopback interface is recommended
[edit interfaces lo0]
ben@R1# show
description "Loopback 0";
unit 0 {
family inet {
address 10.2.2.2/32;
}
family iso {
address 49.0000.0100.0200.2002.00;
}
}
set interfaces lo0 description "Loopback 0"
set interfaces lo0 unit 0 family inet address 10.2.2.2/32
set interfaces lo0 unit 0 family iso address 49.0001.0100.0200.2002.00

## Slide 5: 2. ISO Family on Logical Interfaces
[edit interfaces ge-0/0/4]
ben@R1# show
per-unit-scheduler;
vlan-tagging;
mtu 1950;
unit 3905 {
description “IS-IS tagged interface";
vlan-id 3905;
family inet {
address 10.0.21.2/30;
}
family iso;
}
set interfaces ge-0/0/4 vlan-tagging
set interfaces ge-0/0/4 mtu 1950
set interfaces ge-0/0/4 unit 3905 description “IS-IS tagged interface"
set interfaces ge-0/0/4 unit 3905 vlan-id 3905
set interfaces ge-0/0/4 unit 3905 family inet address 10.8.26.201/30
set interfaces ge-0/0/4 unit 3905 family iso

## Slide 6: 3. IS-IS protocol configuration
If a NET address was configured on the loopback interface, no NET address needed on the logical interfaces running IS-IS
[edit protocols]
ben@R1# show
isis {
level 2 disable;
interface ge-0/0/4.3905;
interface ge-0/0/0.0;
interface ge-0/0/1.0;
interface lo0.0;
reference-bandwidth 1000g;
}
set protocols isis level 2 disable
set protocols isis interface ge-0/0/4.3905
set protocols isis interface ge-0/0/0.0
set protocols isis interface ge-0/0/1.0
set protocols isis interface lo0.0
set protocols isis reference-bandwidth 1000g

## Slide 7: 4. SRX Forwarding Mode
Since SRXs are firewall devices by design, the default forwarding mode is flow-mode
  This will drop all traffic if an interface is not assigned to a security zone
  Most devices running IS-IS will be functioning as routers rather than stateful firewalls and thus should have the forwarding mode set to packet-based
[edit security]
ben@R1# show
forwarding-options {
family {
mpls {
mode packet-based;
}
iso {
mode packet-based;
}
}
}
set security forwarding-options family mpls mode packet-based
set security forwarding-options family iso mode packet-based