## Slide 1: JNCIS-ENT
Border Gateway Protocol (BGP)

## Slide 2: BGP Overview
The routing protocol of the internet
1

## Slide 3: What is BGP?
BGP is the routing protocol of the internet
BGP is commonly used as an Exterior Gateway Protocol
  It can also be used an an IGP
Commonly called a Path Vector dynamic routing protocol
  Due to the AS Path used as the loop prevention mechanism
Highly scalable and capable of exchanging millions of routes
  BGP speaking routers exchange Network Layer Reachability Information (NLRIs)
When used as an EGP, exchanges routes between ASs
  An AS is a network under a single administrative domain
Defined in RFC 4271
  Supersedes RFC 1771
BGP uses TCP as the transport protocol to establish connectivity
  TCP port 179

## Slide 4: Why Use BGP?
BGP is typically used in an enterprise when multi-homed to multiple ISPs
  When single homed, or multi-homed to a single ISP, an enterprise will typically use static default routes with a next-hop of the ISP
When using a single ISP, typically a non-portable subnet is used
  A non-portable add subnet is one owned by the ISP and cannot be used by the enterprise with another ISP unless a Letter of Authorization (LoA) is obtained
  A portable subnet is one that the enterprise has registered and purchased, it may be advertised by the enterprise to any ISP
BGP can provide maximum policy-based flexibility to influence egress and ingress traffic flows for a particular autonomous system

## Slide 5: eBGP vs. iBGP
eBGP is external BGP and represents BGP peering between autonomous systems
  eBGP is most common in the enterprise
iBGP is an internal BGP peering, between routers within the same autonomous system
  iBGP is found within enterprise networks sometimes, though not as common
eBGP peering messages have a TTL of 1 by default
  This expects the peers to be directly connected. If they are not directly connected, then multi-hop must be configured to allow the peerings to establish
eBGP peerings are typically established using interface IPs, whereas iBGP peerings are typically established using loopback interface IPs

## Slide 6: BGP Loop Avoidance
BGP NLRIs include a list of ASs that the path to the destination passes through
  If the AS of the of the receiving router appears in the AS path, the route is dropped
  This prevents routing loops in BGP
iBGP peers will not advertise routes learned from one iBGP peer to another iBGP peer
  The mechanism is called BGP Split Horizon
  Creates a full-mesh peering requirement if other scaling mechanisms are not used

## Slide 7: BGP Peering
Unlike other IGPs, BGP does not have a dynamic neighbor discovery mechanism
  Neighbors must be manually configured
BGP operates over TCP port 179
  TCP is used as the transport protocol to ensure reliable delivery of BGP packets
Since iBGP peers are typically configured between loopback interface addresses, an IGP is required to provide loopback connectivity