## Slide 1: JNCIS-ENT
High Availability (HA)

## Slide 2: What is HA
What it means to be highly available
1

## Slide 3: What is Availability?
Availability is defined as some system resource being able to properly serve users of the system
In the case of digital systems, this may be internet websites, video games, music, movies, software or other types of services delivered over computers and networks
When the resource is not able to properly deliver the intended service, it is said to be unavailable
  The period when the resource is unavailable is considered downtime
  The period when the resource available deliver intended service to the users is uptime
Availability is typically measured as a percentage of downtime over a given period
Availability % | Downtime per year | Downtime per month | Downtime per week
99% | 36.5 days | 72 hours | 16.8 hours
99.9% | 3.65 days | 7.2 hours | 1.68 hours
99.99% | 8.76 hours | 43.2 minutes | 10.1 minutes

## Slide 4: What is a Failure?
A network infrastructure or device failure indicates a cease of normal operation
  This failure may or may not impact traffic flow immediately, in the case of a failed chassis fan or power supply.
A failure that impacts availability is one such that production traffic is not flowing as expected
A impacting failure will typically cease traffic flow, though may cause malformed traffic to flow
  Checksums and other error checking at various protocol layers help ensure the detection of malformed traffic

## Slide 5: High Availability
A highly available network is a subjective term which may have many definitions.
Typically, this is defined as a network which may continue to forward production traffic at an acceptable rate even after at least 1 detected major failure.
  A failure may be purposeful, like in the case of a software or hardware upgrade or replacement.
Many Junos devices support various hardware and software features that increase availability
  Redundant hardware components such as Routing Engines (REs) and fans or power supplies
  Software protocols like GR, GRES, NSR, VRRP and others support increased availability by allowing normal traffic flows in the event of a major failure.

## Slide 6: HA Features
HA Feature | Description
GRES | Graceful Routing Engine Switchover allows interfaces to remain up in the event of a switchover from one redundant routing engine to another. Note, control plane information is not maintained
NSR | Nonstop Routing maintains control plane information and is used with GRES to allow seamless transition from one RE to another
NSB | Similar to NSR, Nonstop bridging synchronizes layer 2 control plane information between REs
BFD | Bidirectional Forwarding Detection is keepalive mechanism to validate bidirectional forwarding capability between two nodes
VRRP | Virtual Router Redundancy protocol is a first hop redundancy protocol used to ensure gateway availability
ISSU | In Service Software Upgrade is a procedure which uses NSR and GRES to perform a Junos software upgrade on a device with redundant REs with minimal network impact
LAG | Link Aggregation Groups form bundles of links to to act as a single higher bandwidth link at layer 2. If a single link in the bundle fails, the bundle can remain active with minimal disruption
RTG | Redundant Trunk Groups allow for the configuration of a redundant uplink from a switch for fast failover without waiting for XSTP convergence
VC | Virtual Chassis can allow single routing engine devices to utilize multiple routing engines for greater availability