## Slide 1: JNCIS-ENT
High Availability (HA)

## Slide 2: Virtual Chassis
Modular highly available hardware
4

## Slide 3: What is Virtual Chassis?
Virtual Chassis, also known as a switch stack by many, allows for the combination of multiple EX series switches into a single logical device
  All control plane functions are handled by an elected routing engine
Virtual Chassis are managed as a single logical chassis
  Configurations applied to the RE will control all line cards
  Software upgrades applied to the RE will be distributed to all line cards
To create a virtual chassis, EX series switches must be physically connected by VC ports
  A virtual chassis may be formed through the dedicated QSFP+ Virtual Chassis Ports (VCPs) or by configuring 10G uplink ports to function as a VCP
Ring
Braided Ring

## Slide 4: Properties of a Virtual Chassis
The first switch powered on will assume the member ID of 0 unless pre-provisioned
  The member ID will function as the slot number when applying interface configuration
  Pre-provisioning involves setting a specific member ID to a VC member using the serial number
When a virtual chassis is created, one of the switches will be elected as the primary routing engine (RE0) and another as the backup (RE1). The remaining switches will act as line cards
  The REs have PFEs built-in and will continue to perform forwarding functions as well
Maximum of 10 member switches in a VC (Member ID 0-9)
Member 0
Member 1
Member 2
Member 3
RE0
RE1
LC0
LC1

## Slide 5: Dynamic Virtual Chassis
No configuration is necessary to form a virtual chassis
  Simply Connect the EX series switches VC ports and power on the switch intended to be the primary
  Once the primary is booted, power on the intended backup RE
  Once the backup is booted, power on the remaining switches
  The switches will dynamically discover the VC
It is recommended best practice to at least explicitly configure the primary and backup RE
  Configure using the following command
  set virtual-chassis member {member-id} mastership-priority {priority#}
  The primary will be member 0 and the backup member 1. Recommended priority is 255
All switches in a VC must be running the same version of Junos
  This may be bypassed by configuring a feature that will automatically update switches with a software mismatch
  set virtual-chassis auto-sw-update
Adding a standalone switch to a VC is as simple as connecting the VC ports
  The new switch will be inactive if not running the same Junos version and auto-sw-update is not enabled

## Slide 6: Configuring Virtual Chassis
By default, the QSFP+ ports on the back of the switch are configured as VCPs
  These are present on the EX4300 and EX3400 models
  The EX2300 does not have any VCPs configured by default
  The EX4100 uses SFP28 ports on the front as VCPs by default
10G/40G uplink ports may be configured as additional VCPs using below command
request virtual-chassis vc-port set pic-slot # port #
show virtual-chassis vc-port

## Slide 7: Configuring a Virtual Chassis cont.
Switches may be pre-provisioned in a VC by specifying the member’s serial number and role in the primary RE’s configuration
  set virtual-chassis member # role [line-card routing-engine] serial-number PG0123456789
When configuring the VC as pre-provisioned, power on and configure the primary RE first with the pre-provisioned members and then connect and power on the member switches
When configuring a VC with only 2 members, recommended best practice to enable no-split-detection
  set virtual-chassis no-split-detection
  Split detection allows the VC to detect when a section of the VC has been separated
  Disabling no-split-detection when configuring a 2 member VC ensures the members will maintain the correct roles if a split and re-merge occur
PG0123456789
PG0293847561
PG1324576890
PG9786352410
{0} routing-engine
{1} routing-engine
{2} line-card
{3} line-card
PG0123456789
PG0293847561
PG1324576890
PG9786352410
Split
PG0123456789
PG0293847561
PG1324576890
PG9786352410
Merge

## Slide 8: Managing a Virtual Chassis
All member switches run the virtual console process that will forward the console port to the primary RE
  Connecting a console cable to any of the member switches will provide console access to the current RE of the VC
The OOB Management ports on each participating switch will go to a virtual management interface with the vme prefix.
  All switches in the VC are managed by the single IP, which will provide a management session to the current RE
  Any switch in the stack may respond on the vme interface and forward the session to the RE
PG0123456789
PG0293847561
PG1324576890
PG9786352410
{0} routing-engine
{1} routing-engine
{2} line-card
{3} line-card

## Slide 9: NSSU
Nonstop Software Upgrade is essentially the same concept as ISSU for redundant RE routers though is for redundant RE switches
  More configuration requirements for NSSU than ISSU
Must satisfy the following configuration requirements
  VC must be connected in a ring, as opposed to a braided ring
  RE0 and RE1 must be adjacent switches, directly connected to one another in the VC
  Line cards must be pre-provisioned as opposed to dynamically provisioned
  In a 2 member VC, no-split-detection must be configured
  All members must be running same version of Junos
  NSR and GRES must be running, optionally also NSB
request system software nonstop-upgrade

## Slide 10: Virtual Chassis Traffic Flow
When a VC is formed, each switch in the VC creates a shortest-path map
  Based on bandwidth of VCPs and hop count
Packets will always take the shortest path through the VC links to the destination
PG0123456789
PG0293847561
PG1324576890
PG9786352410
{0} routing-engine
{1} routing-engine
{2} line-card
{3} line-card
ingress
egress